## Slide 1: Network Types

## Slide 2: Local Area Network (LAN)
A Local Area Network (LAN) is a network that connects computers and devices within a limited geographical area, such as a home, office, or building. LANs are characterized by high data transfer speeds and low latency. LANs are commonly used for sharing resources such as printers, files, and internet connections among devices within the same location.

## Slide 3: Contd….
Key Features:
  Limited to a specific area (e.g., office, home).
  High-speed data transfer.
  Uses Ethernet or Wi-Fi for connectivity.
Common Devices in a LAN:
  Routers
  Switches
  Access Points
  Computers and Printers

## Slide 4: Wide Area Network (WAN)
A Wide Area Network (WAN) covers a large geographical area, often spanning cities, countries, or even continents. Unlike LANs, WANs connect multiple smaller networks (like LANs) and typically use public infrastructure such as telephone lines, fiber optic cables, or satellite links.

## Slide 5
Key Features:
  Covers large geographical areas.
  Slower than LANs due to long-distance data transmission.
  Relies on public networks and leased lines.
Examples:
  The Internet
  Corporate WANs connecting different branch offices

## Slide 6: Wireless Local Area Network (WLAN)
A Wireless Local Area Network (WLAN) is similar to a LAN but uses wireless communication instead of wired connections. WLANs allow devices to connect to the network using Wi-Fi, making them more flexible and convenient.

## Slide 7
Key Features:
  Wireless connectivity using Wi-Fi.
  Suitable for mobile devices like smartphones, tablets, and laptops.
  Can be secured using protocols like WPA2 or WPA3.
Common Use Cases:
  Home Wi-Fi networks
  Public hotspots
  Office wireless networks

## Slide 8: Virtual Private Network (VPN)
A Virtual Private Network (VPN) allows users to securely connect to a network over the internet. VPNs use encryption to protect data and ensure privacy, making them essential for remote access to corporate networks or accessing geographically restricted content.

## Slide 9
Key Features:
  Encrypts data for secure transmission.
  Masks the user’s IP address.
  Allows remote access to private networks.
Common Use Cases:
  Remote workers accessing company resources.
  Securing internet connections on public Wi-Fi.
  Bypassing geo-restrictions.

## Slide 10: Transmission Control Protocol (TCP)
TCP is a reliable, connection-oriented protocol used to transmit data between devices. It ensures that data packets are delivered accurately and in the correct order.

## Slide 11
Key Features:
  Reliable and connection-oriented.
  Ensures error-checking and data integrity.
  Used in applications where accuracy is critical (e.g., web browsing, email).
Common Uses:
  HTTP/HTTPS
  FTP (File Transfer Protocol)
  Email protocols (SMTP, IMAP, POP3)

## Slide 12: User Datagram Protocol (UDP)
UDP is a connectionless protocol that is faster but less reliable than TCP. It is used in applications where speed is more critical than accuracy.

## Slide 13
Key Features:
  Connectionless and faster than TCP.
  No error-checking or retransmission.
  Suitable for real-time applications.
Common Uses:
  Video streaming
  Online gaming
  Voice over IP (VoIP)

## Slide 14: Hypertext Transfer Protocol (HTTP) and HTTPS
HTTP is the protocol used to transfer web pages and other resources over the internet. HTTPS is the secure version of HTTP, which uses encryption (SSL/TLS) to protect data during transmission.

## Slide 15
Key Features of HTTP:
  Transfers web pages, images, videos, etc.
  Stateless protocol (each request is independent).
Key Features of HTTPS:
  Encrypts data for secure communication.
  Uses SSL/TLS certificates to establish trust.
Common Uses:
  Accessing websites
  Transmitting data securely

## Slide 16: Client-Server Basics
The client-server model is a fundamental concept in networking, where a server provides resources or services, and a client requests them.

## Slide 17: Client
A client is a device or application that initiates a request to a server. The client sends a request, and the server responds with the requested resource or service.
Examples:
Web browsers (clients) requesting web pages from a web server.
Email clients connecting to an email server.

## Slide 18: Server
A server is a system or application that provides resources, data, or services to clients. Servers are designed to handle multiple client requests simultaneously.
Examples:
Web servers hosting websites.
Database servers storing and managing data.
File servers providing file storage.

## Slide 19
Client-Server Interaction Process:
  The client sends a request to the server.
  The server processes the request.
  The server sends a response back to the client.
Benefits of the Client-Server Model:
  Centralized resource management.
  Scalability to handle multiple clients.
  Security through controlled access.